## Slide 1
Test Result DB
Result DB
PC
ALT Instrument
DAQ
Pressure, Flow
Test Result, Test Time
START (Manual)
STOP (Manual)
CLAMP
PASS
FAIL
FAIL
PASS
IDLE
Test
Running
Only 3 DO lines are used in S/W
Where as 4 DO lines are used in H/W

## Slide 2
Result DB
ALT Instrument
START
STOP
CLAMP
PASS
FAIL
FAIL
PASS
IDLE
Test
Running
PC
RS Linx PLC
(Robot)
Barcode Scanner
Read Tag:
Robot_Available
Start_Test
Stop_Test
Scan_Trigger
Station # to Start Test
Read Tag Ack.
Write Tag:
Task_Available_for_Robot
New_Serial
Serial_Adapter_Plate_Size
Serial_Displacement_Size
Serial_Flange_Size
Test_Result
Station_Number
Rerun
Invalid_Serial_Number
Write Tag Ack.
DAQ
Test Select
TTA
TTB
Test Result DB
Pressure, Flow
Test Result, Test Time
Only 3 DO lines are used in S/W
Where as 4 DO lines are used in H/W
Part Detail DB

## Slide 3: New ALTS - PC Behaviour
PC remembers the station occupancy and act accordingly for the new part.
PC directly controls the SELECT line for ALT instrument to select the test type.
PC scans for the new serial after getting scan_trigger from PLC
PC sends the rerun command to Robot and robot acts accordingly (re-clamp part).
PC sends the invalid s.no along with new s.no to intimate the arrival of serial at scanner stage which has no DB entry.
Work order number will be used from INI file

## Slide 4: New ALTS – Robot Behavior
Should act according for Invalid S.No. Move the invalid serial (part) to appropiate location.
Should act accodingly to Test result and rerun command. If rerun is true, robot should send the start signal again for the specific station.

## Slide 5: System Setup
2 scanners for Auto mode & 1 scanner for manual mode
-add to logic
Log results for all retest

## Slide 6: More Questions
We want PLC tags from Eaton
Start signal from ALTS (manual). How PLC will give us in manual mode?
What are the emergency stop signals? How the STOP signal in the existing system is handled?
Retest count is INI configured to 1 retest? It can also be hard coded. Should we still seek from PLC for count?
If we can reduce the user count to 1, there are 4 user entries in DB write. What can we write for User 2, 3 & 4
LeakTek DB configuration
Part ready at scanner. Will it be provided from PLC?

## Slide 7: Clarifications
In existing ALTS, work order number is part of the result written to the SQL Server database. You mentioned that we won’t have work order numbers for the new system. What do we write to the database in lieu of work order number? Do you have to write anything at all? Maybe we should call to have a conversation on this
-use constant for now from.
If the part fails air leak test, we will re-run the test. How many times can you re-run the test? I am assuming that we log the results for all runs in the SQL database (we need to check if there is a timestamp parameter when writing results to the database to distinguish between the different runs). I believe we agreed on 1 retest (Mike please confirm). We do log results for all runs. Maybe we should get together to check that parameter; I’m not sure where to check that…